Functional
1.3.1 Satellite Requirements
- Ability to plug into standard National Electrical Manufacturers Association (NEMA) 5-15 mains electrical outlets
- Must provide at least as many outlets as it covers up
- Less than 5% error on current and voltage reading
- Power draw less than 1Watts (W) per Satellite
- Broadcasts information up to 500Meters (M)
- Transmits every 60 seconds without any
  - Losing readings is considered an error
- Ability to connect to the Server wirelessly
1.3.2 Server Requirements
- Physical Server inside the monitored building
- Runs on less than 10W
- Hosts web server for Display
- Ability to sync Satellites
- Ability to connect to the user's network
- Abililty to connect to Satellites wirelessly
1.3.3 Display Requirements
- User Management
- Add users
- Delete users
- Modify user information
- Modify user permissions
- Group Management1
- Add groups
- Delete groups
- Modify groups
- Group permissions
- Device Management
- Add Devices
- Disable Devices
- Does not include deleting Devices, since that would invalidate history
- Modify Devices
- Rename
- Change outlet association
- Device Groups1
- Device groups are logical groupings of Devices that can be viewed as a single Device in the View Data section
- Create Device groups
- Delete Device groups
- Modify Device groups
- Satellite Management
- Add Satellites
- Remove Satellite
- View Data
- View Device Power Consumption
- Shows the user power consumption on a per-device (or device group) basis
- View Power Consumption Over Time
- Shows the user power consumption over a specified range of time
- Includes total and per-device power consumption
- Be able to compare power usage of devices
- View Device Cost Over Time1
- Shows the user the cost to run a device, or group of devices, over a specified time range
- Shows the user a comparison of device costs over a specified range with a given interval
- E.g. Show them the device cost every month for the past year
- Power Bill Guesstimator1
- View cost to run a specified device over a period of time in the future
- View cost to run multiple devices over a period of time
- View expected power bill if a device is added
- Allow the user to specify cost of power for
- Specific time ranges
- Specific power-usage ranges
- E.g. Power cost the user $0.08 per kW/hr for the first 500
- kW/hrs, and $0.10 after that
- Estimate total power bill for monitored devices
- Factory reset1
- Allow the user to reset the system to default settings via...
- A form
- A physical button located on the server
- Software upgrade1
- Allow the user to upgrade the system to the newest software version

Non Functional
8.1.1 Satellite Requirements
- Able to work in groups of up to 255 for any one Server within a 500 meter radius
- Conveniently sized and shaped
- Unobtrusive
- As small as possible given the hardware
- A small LED near each socked to indicate whether the Satellite is being monitored
- A small LED on each Satellite to indicate power
- A button for turning On or Off
- A button to initiate connection to the Server
- Will be an unobtrusive color other than white
- Tamper proof
- Data sent from Satellite to Server shall be encrypted
- Satellites will cost less than $7.50 (USD) to produce
8.1.2 Server Requirements
- Enough hard drive space to hold 5 years of data
- Supports up to 255 Satellites
- Small and unobtrusive case
- Color shall not be white
- User can add Satellites at any time
- Encryption used on all communication to Satellites
8.1.3 Display Requirements
- Interface is easy to learn
- Must provide a “responsive” interface (responsive is: must provide user with feedback within 300 ms)
- Data is not lost when a device is moved to a new Satellite
- Not vulnerable to SQL injection
- Not vulnerable to XSS
- No unauthorized access
- Data transmitted to the Display is encrypted
- Maximum number of users to connect at any given time is 3
- Satellites shall exist on their own wireless network
- This network shall be insulated from the outside by the server